## Slide 1: PCIe Hot-Plug and Error Handling for NVMe 2019 NVMe™ Annual Members Meeting and Developer Day March 19, 2019 Prepared by: Austin Bolen, Server Storage Technologist, Dell EMC Curtis Ballard, Storage Technologist, HPE Joe Cowan, Senior Systems Architect, HPE

## Slide 2: Agenda
The Importance of Hot-Plug and Error Handling for NVMe™
Challenges with NVMe Hot-Plug and Error Handling
Solutions to NVMe Hot-Plug and Error Handling Challenges
Questions

## Slide 3: The Importance of Hot-Plug and Error Handling for NVMe™

## Slide 4: The Importance of Hot-Plug (RASM)
* https://software.intel.com/en-us/articles/rasm-a-primer-for-isv-applications-engineers
Better RASM = Reduced TCO
Customer Requirements:
Surprise/Async hot-plug
  - No prepare-to-remove
Parity with SAS/SATA or better
Handle all PCIe errors, not just errors due to surprise/async removal

## Slide 5: The Importance of Hot-Plug (Reliability)
* https://software.intel.com/en-us/articles/rasm-a-primer-for-isv-applications-engineers
Reliability:
Device reliability is key, however:
Small failure rates exacerbated at scale
    Hundreds or thousands of systems per datacenter
    Many drives per system
NAND wears out
Failures will occur HA solutions will require Hot-Plug

## Slide 6: The Importance of Hot-Plug (Manageability)
* https://software.intel.com/en-us/articles/rasm-a-primer-for-isv-applications-engineers
Manageability:
Monitoring and reporting of device failure or predicted failure
Inventorying for re-provisioning of storage

## Slide 7: The Importance of Hot-Plug (Serviceability)
* https://software.intel.com/en-us/articles/rasm-a-primer-for-isv-applications-engineers
Serviceability:
Async hot-plug is required for SAS/SATA equivalent serviceability for NVMe drives
Async/surprise removal eliminates the need for:
  Orderly removal software
    A technician with physical access to replace drives may not have access to these software interfaces
  Costly orderly removal hardware (attention buttons, power controllers, etc.)

## Slide 8: The Importance of Hot-Plug (Availability)
* https://software.intel.com/en-us/articles/rasm-a-primer-for-isv-applications-engineers
Availability:
Hot-plug increases availability by avoiding costly downtime due to:
  Replacing failed drives
  Re-provisioning storage

## Slide 9: Challenges with NVMe™ Hot-Plug and Error Handling

## Slide 10: NVMe™ Hot-Plug/Error Handling – Why is it such a heavy lift?
Because it’s an ecosystem issue!
  NVMe Drive
  Platform
    Hardware
    Firmware
    BMC
  PCIe Root Port/Switch
  Operating System
    NVMe Driver
    PCIe Driver
    ACPI Driver
  Applications
Each player historically looking at their own piece. But who is looking at the whole picture?
It’s a rope!
It’s a wall!
It’s a
spear!
It’s a
tree!
It’s a
fan!
It’s a
snake!

## Slide 11: Hot-Plug Storage – A High-Level Comparison
Host Software (Operating System, Drivers, Applications, UEFI/BIOS)
SAS Controller
SATA Controller
NVMe Controller
SAS Drive
SATA Drive
NVMe Drive
Hot-Plug Barrier
Processor
Hardware above the barrier is not hot pluggable
Hardware below the barrier is hot pluggable
SAS Bus
SATA Bus
PCIe Bus
SAS/SATA drivers bind to controllers above the hot plug barrier
Protocol conversion provides software isolation
Physical layer conversion provides hardware isolation
NVMe™ drivers bind to controllers below the hot plug barrier
No protocol translation == No software isolation
No physical layer conversion == No hardware isolation

## Slide 12: The PCIe Hot-Plug Eras (Where we’ve been, Where we are)
The Standard Hot-Plug Controller (SHPC) Era
  Timeframe: PCI/PCI-X, Early PCIe
  Complex (196 page specification)
  Orderly insertion/removal only
    Async insert/removal likely to crash system
  Additional hardware (expensive)
    Power Controllers
    Power/Attention Indicators/Buttons
    Mechanical Retention Latch (MRL)
The Hot-Plug Surprise (HPS) Era
  Timeframe: Starting with new form factors like PCIe storage and Thunderbolt to present day
  New form factors demand a simplified user experience that eliminates orderly removal overhead
    For NVMe, mimic SAS/SATA hot-plug model
  Surprise insertion/removal
    Surprise removal not supported by most OSes
    Software or hardware initiated orderly removal typically required

## Slide 13: Hot-Plug Issues Persist After SHPC and HPS
System crashes are still possible
  Errors if orderly removal process not followed with SHPC
  Synthesized all 1’s data during errors - not always handled correctly by software
  No strict model for interaction of stack components - leads to race conditions causing crashes and deadlocks
Other issues
  Timely detection of removal and insertion (detection while in low power state)
  Mechanical insert/remove issues (slow insert, angled insert, etc.)
  Issues often require changes outside the component under test (OS, switch, etc.)
SHPC and HPS aren’t robust enough for complex use cases
Notes: It takes a long time and is hard working with all the different parties for fixes for issues found when using SHPC and HPS causing delayed time to market and extra expense.

## Slide 14: Solutions to NVMe™ Hot-Plug and Error Handling Challenges

## Slide 15: Key Design Tenets
Create a hot-plug and error handling/recovery “toolbox”
  Allow for flexibility in solution
    Systems, Form Factors, OSes all have different needs
    Support all PCIe use cases, not just NVMe
  Tools to handle unforeseen issues
Fix known issues
Leverage and reach parity with existing solutions
  SAS/SATA model
    Eliminate need for orderly insertion/removal
  Proprietary PCIe error recovery models
Multi-phase approach with incremental improvements
Error recovery mechanisms must be extensible to all PCIe errors
  Surprise/async removal errors
  Minimize the chance of issue due to accidental removal of wrong device
  Errors unrelated to hot-plug
Hot-Plug
&
Error Handling
Hot-Plug &
Error Handling

## Slide 16: Key Design Tenets
Hooks for time-to-market
  System hardware/firmware changes should be sufficient for:
    New system designs and form factors
    Fixing defects/unforeseen issues
  Avoid/minimize need for:
    Future OS changes
    Future PCIe Root Port/Switch changes

## Slide 17: Industry Alignment
Alignment/Feedback from OEMs
  Dell EMC
  HPE
  Lenovo
  Oracle
Alignment/Feedback from PCIe Root Port and Switch Vendors
  AMD
  Broadcom
  Intel
  Microsemi
OSVs
  Microsoft
  VMWare
  Linux distributors/kernel developers

## Slide 18: Standards-Based Solution
ECN Sponsors | Standards Bodies | Specifications
Proposal | Standard | Stage | Description
System Firmware Intermediary (SFI) | PCIe Base Spec | Ratified. ECN Published to PCI-SIG Website. | Adds system firmware layer between OS and PCIe devices for hot-plug.
Containment Error Recovery (CER) | PCIe Base Spec | Ratified. ECN Published to PCI-SIG Website. | Defines software/firmware PCIe error recovery model built on top of Downstream Port Containment hardware.
 | ACPI Spec | Released In ACPI 6.3 | 
 | PCI Firmware Specification | Ratified. ECN Published to PCI-SIG Website. | 
Hot-Plug Extensions (_HPX) | ACPI Spec | Released In ACPI 6.3 | Allows system firmware to tell OS how to set PCIe Configuration Space for hot-inserted PCIe devices.
 | PCI Firmware Specification | Member Review Complete. Should be ratified shortly. | 

## Slide 19: CER Era
Host SW/FW (Operating System, Drivers, Applications, UEFI/BIOS)
PCIe Root Port w/ DPC
NVMe Drive
Processor
PCIe Bus
Error
PCIe Root Port w/ DPC
Switch Upstream Port
Switch Downstream Port w/ DPC
Switch Downstream Port w/ DPC
NVMe Drive
NVMe Drive
Async Removal or other errors detected by the Root Port or Switch
DPC in Root Port or Switch contains errors by forcing/keeping PCIe link down
1
2
3
4
5
The Root Port or Switch notifies FW or host OS
FW and/or host OS entities attempt to recover from the error
PCIe Bus
PCIe Bus
Async Remove
Host OS releases DPC and restarts device if present and recovered
PCIe
Switch
The Containment Error Recovery (CER) Era
  Timeframe: Transitioning now
  Replaces HPS
  The term “async” replaces “surprise” (i.e. async removal/insertion instead of surprise insertion/removal) in PCIe specs
  CER software/firmware model can be used to recover from many PCIe errors – not just errors due to async removal
  Utilizes Downstream Port Containment (DPC) hardware in PCIe root ports and switch downstream ports to contain errors including async remove related errors
  Two CER modes: Native OS Controlled and Firmware First
    Firmware First mode requires ACPI changes in OS and BIOS/UEFI
  Based on tried-and-true proprietary models

## Slide 20: System Firmware Intermediary Era
Host Software (Operating System, Drivers, Applications, UEFI/BIOS)
SAS Controller
SATA Controller
NVMe Controller
SAS Drive
SATA Drive
NVMe Drive
Hot-Plug Barrier
Processor
Hardware above the barrier is not hot pluggable
Hardware below the barrier is hot pluggable
SAS Bus
SATA Bus
PCIe Bus
System Firmware Intermediary (SFI)
SFI isolates PCIe hot-plug events from the OS, drivers, and applications for hot-plug - does not alter data path.
Hardware isolation in PCIe Root Ports and Switch Downstream Ports
Provides options to invoke system firmware (BIOS, UEFI, BMC, etc.) for hot-plug events
Particularly useful for complex out-of-band (independent of host OS) platform config of hot-inserted devices (e.g., unlocking TCG drives or device authentication)
The System Firmware Intermediary (SFI) Era
  Timeframe: Silicon support will arrive over next several years
  Does not replace DPC/CER - works alongside DPC/CER
  Adds hardware/firmware layer between OS and devices for hot-plug

## Slide 21: Hot-Plug Parameter Extensions (_HPX)
_HPX exists across all hot-plug eras
_HPX allows system firmware to provide system-specific PCIe config space settings to OS
  Not just for hot-inserted device; also used if device is reset at runtime
New _HPX Setting Record (Type 3) defined in ACPI specification
  Previous setting records only worked for pre-defined registers
  New registers required spec update an OS change
  New Type 3 record can specify any register with offset relative to offset 0h of:
    The start of configuration space
    A Capability Structure
    An Extended Capability Structure
    A Vendor-Specific Extended Capability
    A Designated Vendor-Specific Extended Capability
Handle different revisions of capability structures
  Apply changes to any revision of the capability structure
  Apply changes to a specific revision of the capability structure
  Apply changes to capability structures with revision greater than or equal to the specified revision
Supports simple if-then-else conditional grammar
  E.g., to set PCIe configuration space registers to preferred value based on device capability
Lightweight alternative to SFI for simple config space settings
Example Pseudocode – Set Completion Timeout (CTO) Value based on device’s Completion Timeout Ranges Supported:
If CTO Range B supported then
Set CTO Value to 65 ms to 210 ms
Else if CTO Range C supported then
Set CTO Value to 260 ms to 900 ms
Else if CTO Range D supported then
Set CTO Value to 4 s to 13 s
Else
Set CTO Disable

## Slide 22: Next Steps
PCIe Root Ports and Switches
  Add support for DPC/eDPC
  Add support for SFI
Operating Systems and OEMs
  Add support for async removal in HPS mode as a stop-gap until CER can be fully implemented
  Add support for Containment Error Recovery Model defined by PCI-SIG
    Native OS controlled and Firmware First models
  Review/contribute to open source effort
    DPC Containment Error Recovery patches submitted to Linux kernel
      Also called Error Disconnect Recover (EDR) after the ACPI method used in DPC CER model
    _HPX patches submitted to Linux kernel
Connectors/Form Factors - Design for async hot-plug
  Prevent damage to I/O pins on hot-insert typically by making ground pins longer than other pins
  Limit current surge on hot-insert
    Pre-charge pin for each voltage rail which is second to mate or
    Soft start/hot-plug circuits for each rail
  Physical presence mandatory
    Should be shortest pin so platform knows when device is fully inserted
    May need a presence pin on each end of connector unless you can guarantee connector cannot mate at an angle
  Make sure pins can’t cross-connect on insert
  Consider issues with pin wipe b/c higher frequencies demand shorter pin lengths making it difficult to support pins of different length
  Form factors should allow for stable insert/removal
  Form factors should allow adequate mount points

## Slide 23: Resources
Resource | Link
ACPI 6.3: Add “Error Disconnect Recover” mechanism for DPC and new Hot-Plug Parameter Extensions (_HPX) Setting Record (Type 3) | https://uefi.org/sites/default/files/resources/ACPI_6_3_final_Jan30.pdf (DPC EDR) https://mantis.uefi.org/mantis/view.php?id=1939* (_HPX) https://mantis.uefi.org/mantis/view.php?id=1922*
PCI Express Base Specification Revision 4.0 Version 1.0 | https://members.pcisig.com/wg/PCI-SIG/document/10912?downloadRevision=active*
PCIe Base Spec. ECN: Async Hot-Plug Updates (DPC/CER, SFI) | https://members.pcisig.com/wg/PCI-SIG/document/12400*
PCI Firmware Spec. ECN: Downstream Port Containment related Enhancements | https://members.pcisig.com/wg/PCI-SIG/document/12614*
PCI Firmware Spec. ECN: _HPX and PCIe Completion Timeout related _OSC Enhancements | https://members.pcisig.com/wg/PCI-SIG/document/12712*
Dell EMC Tech Note: NVMe Hot-Plug Challenges and Industry Adoption | https://downloads.dell.com/manuals/common/dfd_-_nvme_hot-plug_challenges_and_industry_adoption.pdf
Implementing Hot-Plug in NVMe Storage Systems | https://www.flashmemorysummit.com/English/Collaterals/Proceedings/2018/20180808_NVME-201-2_Yung.pdf
The Modernization of PCIe Hot-Plug in Linux | https://lwn.net/Articles/767885/
* Requires member access to the relevant standards body website

## Slide 24: Linux Enablement
Feature | Patch | Link
DPC Containment Error Recovery (CER) | Add Error Disconnect Recover (EDR) support | https://patchwork.kernel.org/cover/10833723/
 | Add _OSC based negotiation support for DPC | https://patchwork.kernel.org/patch/10833717/
 | Add Error Disconnect Recover (EDR) ACPI notifier support | https://patchwork.kernel.org/patch/10833725/
 | Add Error Disconnect Recover (EDR) support | https://patchwork.kernel.org/patch/10833721/
Hot-Plug Parameter Extensions (HPX) | Implement support for _HPX Type 3 tables | https://patchwork.kernel.org/cover/10843875/
 | Do not export pci_get_hp_params() | https://patchwork.kernel.org/patch/10843877/
 | Remove the need for 'struct hotplug_params’ | https://patchwork.kernel.org/patch/10843887/
 | Implement Type 3 _HPX record | https://patchwork.kernel.org/patch/10843883/
 | Advertise HPX type 3 support via _OSC | https://patchwork.kernel.org/patch/10855469/

## Slide 25: Questions?